Knock Lock Program documentation

The button will be on PORTB0. The locking solenoid will be on PORTB1. We want the button to be an input (0) and the solenoid to be an output (1), Thus, the DDRB register should be set as 0x02:

Bit 7	Bit 6	Bit 5	Bit 4	Bit 3	Bit 2	Bit 1	Bit 0
0	0	0	0	0	0	1	0
0				2

The button needs to use pull up resister mode, and the solenoid must be initially off. To do this, we need PORTB1 to be off, and PORTB0 on. This makes it so that the button pulls to ground when it is pressed. The PORTB register looks like this when the solenoid is off:

Bit 7	Bit 6	Bit 5	Bit 4	Bit 3	Bit 2	Bit 1	Bit 0
0	0	0	0	0	0	0	1
0				1

Similarly, when the solenoid is on, the PORTB register looks like this:

Bit 7	Bit 6	Bit 5	Bit 4	Bit 3	Bit 2	Bit 1	Bit 0
0	0	0	0	0	0	1	1
0				3

The PINB register holds the current state of the ports. In this case, when the button is pressed, bit 0 will be a 0, and when it is not pressed, it will be a 1. The mask we need to check if the bit is set is 0x01.

For the timer, we need to set the CTC bit in the TCCR0A register. This will clear the timer and restart it every time the timer reaches the value we want.

We then need to set the pre-scaler to 64 in the TCCR0B register. To do this, we set CS01 and CS00 to a 1. This starts the clock.

Setting the OCR0A (compare) register to 125 makes the timer generate an interrupt every 1ms. Can use this site here to calculate the ticks: http://eleccelerator.com/avr-timer-calculator

To enable an interrupt every time our compare value is met, we need to set bit OCIE0A in the TIMSK0 register. We also need to include the <avr/interrupt.h> library and use the sei() function to set the interrupt enable flag.

The ISR() function is the interrupt service routine. This is what is used to increment the counter for how many milliseconds we are currently at. We need to use TIMER0_COMPA_vect in the ISR() to check for the interrupt.

Currently, the maximum number of knocks is 10. That could change, though. The function that compares the two knock sequences will have a threshold in the future that will make it easier to get the same knock sequence. The function that checks the code returns 0 on success, 1 when # of knocks don't match, and 2 when the knock times don't match.

Use the ADMUX register to setup the A to D converter reference voltage and choose the correct signal. I'm using signal 5 currently and we need to set bit 6 to a 1 and bits 2 and 0 to a 1 for channel 5.

Next, need ADCSRA register. The ADC uses interrupts, so we set that here. We need to set ADEN, which enables the ADC. Also need to set the ADIE bit to enable interrupts from the ADC. We then need to set the pre-scalar value to the max of 128. To do this, set ADPS0-2.

Final thing we need is to disable digitial input buffer in the DIDR0 register. To do this, set the ADC5D bit in the register.

When a knock sequence is accepted, we write the knock number and the knock times to eeprom in case the device loses power. In address 0x00 of eeprom we write the knock number. Starting at address 0x04, we write the knock time values. Setting address 0x00 to 0 will effectively “clear” the eeprom since the program will not read the knock times. The knock times at this point are considered junk.